## Slide 1
SENTINEL
Unified Viewing & Metadata Analytics
Gujarat Police Innovation Challenge 2026 · Model 2
Built by RuVision Thinking Labs

## Slide 2
BACKGROUND
The Problem
▸ 26 Government Departments operate independent CCTV systems — different vendors, VMS platforms, storage architectures, and retention periods (7 to 15+ days).
▸ Central command centres must access these feeds through multiple separate viewer systems — no single pane of glass.
▸ High-value law-enforcement databases already exist and are digitized — VAHAN (vehicle registration), eGujCop / CCTNS (stolen vehicles, wanted persons), AFIS / NAFIS — but they are siloed from live video.
▸ Result: no automated, real-time correlation between what a camera sees and what these databases already know.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
2

## Slide 3
SOLUTION MODEL
Model 1 (Foundation) + Model 2 (Primary) — Registry & GIS Foundation with Unified Viewing & Metadata Analytics
▸ Direct RTSP / ONVIF / vendor-API connection to each camera or VMS.
▸ No middleware or federation layer introduced.
▸ Departmental VMS and storage systems remain completely untouched and continue operating independently.
WHY MODEL 2, NOT 3/4
▸ 26 departments' VMS/storage diversity makes a federation layer a multi-department program — not a hackathon-timeline build.
▸ Delivers exactly the two capabilities the evaluation tests: live unified view + AI vehicle tracing.
▸ Lowest integration risk: zero dependency on any department changing its systems.
▸ Model 1 (Registry & GIS Foundation) is built underneath as the mandatory foundation every submission requires.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
3

## Slide 4
MANDATORY FOUNDATION, BUILT UNDERNEATH
Model 1 Foundation — Registry & GIS
▸ Camera registry auto-synced from the live catalogue — all 30 sandbox cameras, zero manual entry.
▸ Two additional onboarding paths demonstrated: CSV bulk-import and a manual single-camera entry form.
▸ Department and camera type are inferred from location-name patterns (toll/gate/bypass/junction) — the same signal already validated in our plate-legibility findings.
HONEST STATUS
▸ GIS map: 23 of 30 cameras geocoded and plotted; 7 failed on genuinely ambiguous location names and are omitted from the map, not guessed — still visible in the registry table.
▸ Caught one bad match during development (a location name that resolved to Kashmir); rejected by a Gujarat bounding-box check before it could reach the map.
▸ Department/camera-type mapping is illustrative, inferred from naming patterns — not department-supplied ownership data.
GAP ANALYSIS
▸ Disconnected-camera count and stale-detection count, both live.
▸ ANPR-viability breakdown by camera type: toll/gate/bypass viable vs. wide junction cameras situational-only.
▸ Surfaces the same camera-angle finding from our AI-analytics debugging story as an operational coverage view.
[SCREENSHOT: Registry tab — map view]
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
4

## Slide 5
ARCHITECTURE
End-to-End Data Flow
Departmental CCTV / VMS
→
Capture Layer
→
ANPR Analytics
→
Watchlist & Alerting
→
Route Reconstruction
→
Unified Dashboard
No video is ever centrally stored — only structured detection metadata (plate text, camera, timestamp, confidence).
▸ Capture: TCP-forced RTSP, PTS-derived timing, exponential-backoff reconnect.
▸ Analytics: YOLO plate detector + PaddleOCR, CPU-only, configurable sample rate.
▸ Storage: SQLite metadata log (schema-compatible upgrade path to PostgreSQL).
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
5

## Slide 6
ENGINEERING — PROVEN, NOT JUST DESIGNED
Live Stream Ingestion
▸ TCP-forced RTSP, PTS-derived timing (never wall-clock or declared FPS), exponential backoff reconnect.
▸ Tolerant of decoder warm-up noise and mixed H.264 / H.265 codecs — confirmed live on the sandbox grid.
▸ Camera inventory always pulled live from the gateway catalogue — zero hardcoded camera IDs.
VALIDATED AGAINST THE LIVE 30-CAMERA SANDBOX
▸ Found and fixed a real cross-thread cv2.VideoCapture segfault during load testing — a genuine stability bug, not a hypothetical one.
▸ Confirmed automatic reconnect/recovery after a forced restart.
▸ Ran a clean, multi-camera, multi-hour unattended session: zero crashes, zero unwanted reconnects, 480+ real detections logged.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
6

## Slide 7
AI-POWERED VIDEO ANALYTICS
Finding — and Fixing — the Plate-Legibility Bottleneck
1
Most sandbox cameras are wide-angle overhead junction cams — genuinely not plate-resolvable at distance. An honest finding, not a failure.
2
Went back to the camera catalogue's own display names and found a toll-plaza camera ("Tollnaka") — camera metadata, not just camera count, was the actionable signal.
3
On that camera's legible plate crop, our first OCR engine (EasyOCR) capped at ~0.3 confidence after heavy tuning. Swapping to PaddleOCR on the identical crop, no other change: 0.87 confidence.
4
Even then the real pipeline still failed — root cause was our own bounding-box crop clipping characters. Fixed by padding the detector's box 75% of its own size, verified against real detector output.
5
Result over a multi-hour unattended run: 480+ detections above threshold across three independently-confirmed cameras — full plausible Indian plates, not fragments (e.g. GJ05AU9828 at 0.96 confidence).
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
7

## Slide 8
AI ANALYTICS — LIVE EVIDENCE
Detection Feed: Watch the AI Working in Real Time
Real crop + real annotated frame (bounding box drawn by the detector) for two different live-detected vehicles — not staged.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
8

## Slide 9
WATCHLIST CORRELATION
Real-Time Alerting
▸ Every OCR read — not sampled after the fact — is normalized and matched immediately.
▸ Two-pass matching: exact + OCR-confusion-aware pass (0/O, 1/I, 5/S, 8/B, 2/Z), then fuzzy-similarity fallback.
▸ A match writes an alert with camera, plate, PTS timestamp, confidence, and matched entry — visible on the dashboard within seconds, no manual refresh.
▸ Designed to plug into VAHAN / eGujCop-CCTNS as the real watchlist source in production; a representative watchlist is used for this demo, as explicitly permitted.
Real watchlist match — 100% confidence, real plate crop, real timestamp.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
9

## Slide 10
THE EVALUATION'S CORE TEST
Vehicle Route Reconstruction
▸ Given a plate, returns every (camera, location, timestamp) detection in chronological order.
▸ Cross-camera candidate found: plate GJ18ZT1282 detected on cam06 (Timbavadi gate, Junagadh) and cam22 (BK Mervada tran Rasta) ~26 hours apart, OCR confidence 0.95 and 0.87 — linked via the same Z/2 confusion-variant matching already used for the single-camera case below.
Real search result — visual timeline with plate crop.
HONEST STATUS
▸ Three cameras independently confirmed ANPR-viable, ran for days, 21,000+ real detections.
▸ One cross-camera candidate found via exact + confusion-variant matching (GJ18ZT1282 / GJ182T1282, cam06 <-> cam22): a strong OCR-level match, not database-verified as the same physical vehicle — reported as candidate evidence, not certainty.
▸ The confirmed, unambiguous trace remains the single-camera case: one vehicle detected 4 times within 16 seconds on cam12, correctly linked across BV2807 / 8V2807 OCR readings.
▸ A map view of the same route is now available alongside this list view, plotted using the Model 1 registry's camera coordinates.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
10

## Slide 11
UNIFIED CONTROL-ROOM VIEW
The Dashboard
Camera grid — live thumbnails, last-seen plate per camera.
Watchlist administration.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
11

## Slide 12
IMPLEMENTATION
Technology Stack
Capture
OpenCV + FFmpeg backend (Python)
Detection
Ultralytics YOLO — pretrained, CPU-only
OCR
PaddleOCR (PP-OCRv6)
Storage
SQLite (pilot); schema-compatible path to PostgreSQL
Dashboard
Streamlit, custom dark theme
No GPU, no external message bus required at this scale — deliberately minimal-dependency for fast, reliable deployment.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
12

## Slide 13
PATH TO STATEWIDE SCALE
Scalability, Security & Deployment
▸ Horizontal scale-out: independent capture/ANPR workers, sharded by camera set — no component assumes a single-machine camera count.
▸ Edge pre-filtering + GPU/accelerator path is the realistic route to ~80,000-camera scale; this prototype's frame-sampling and confidence knobs are exactly what moves to edge-side config.
▸ Credentials never logged (verified in code); consume-only design — never pushes to or controls any gateway.
▸ No department's existing VMS, storage, or retention policy is touched.
▸ RBAC, audit logging, and TLS-everywhere are the production hardening path beyond this prototype.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
13

## Slide 14
EXPECTED OUTCOMES
Operational Benefits
▸ Single pane of glass across departments — without a multi-year federation program.
▸ Automated, continuous watchlist correlation — proactive alerting instead of manual after-the-fact video review.
▸ Fast, low-risk path to statewide expansion: same architecture, more camera shards, no redesign required.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
14

## Slide 15
HONEST ABOUT CURRENT SCOPE
What's Next
▸ Face Recognition (FRS) and other analytics — explicitly out of scope for this build, bonus territory.
▸ Live VAHAN / eGujCop integration — currently a representative demo watchlist, as explicitly permitted by the challenge rules.
▸ Edge deployment pilot for bandwidth-constrained districts.
SENTINEL — Gujarat Police Innovation Challenge 2026 · Model 2
15

## Slide 16
Thank you
SENTINEL — Unified Viewing & Metadata Analytics